Analytical X-ray Safety

This quiz is designed to test your understanding of the MS Powerpoint Slide presentation

Quiz

1. The background radiation in New Zealand is about _____ mSv per year

- 0.5

- 1.2

- 1.8

- 2.4

- 3.0

2. The maximum allowable effective dose to a radiation worker is _____ mSv per year above background

- 5

- 20

- 100

- 150

3. Alpha, gamma and x ray radiation have a radiation weighting factor of _______ respectively

    - 10, 1, 1

    - 20, 2, 1

    - 20, 1, 1

    - 20, 5, 5

4. The maximum allowed effective dose to the general public is ____ mSv per year above background

- 1

- 5

- 15

- 50

5. The unit of measure of exposure is the

- Roentgen

- Rad

- Gray

- Sievert

6. The SI unit of measure of dose is the

- Roentgen

- rad

- Gray

- Sievert

7. The SI unit of measure of equivalent dose is the

- rem

- rad

- Gray

- Sievert

8. The Equivalent Dose is the multiple of the

- Exposure and radiation weighting factor

- Dose and radiation weighting factor

- Dose and tissue weighting factor’

- Exposure and dose

9. A 0.5 Gray dose of x-ray radiation is roughly equivalent to an effective dose of

- 0.5 Gray

- 0.5 Sieverts

- 1.0 Sieverts

- 10 Sieverts

10. The majority of damage due to ionising radiation at a molecular level arises from the hydroxyl free radical.  True or False

11. ALARA means

- As low as readily achievable

- Always low and readily accessible

- Always low and really achievable

- As low as reasonably achievable

12. Which of the following is a compliance measure and NOT a requirement for SAFE use of x-ray equipment

- Operators must be trained in safe use of the x-ray equipment

- X-ray leakage and scatter must be measured periodically

- Safety interlocks are checked regularly

- Machine must have current licence holder.

13. Which of the following is MOST relevant to safe operation of analytical x-ray equipment:

        - Reduce time spent next to machine

        - Follow manufacturer's instructions as well as verifying interlocks functioning and shielding is adequate

        - Increase distance away from machine

        - Logging all repairs

14. The Regulatory body concerned with Safe Use of Ionising Radiation is:

              - Office of Radiation Safety

              - National Radiation Laboratory

              - ESR

              - Ministry of Health.